## Slide 1: ICD10-PCS Coding Proposal for Aptus® Heli-FXTM Procedure
Kathy Smith, CPC
Sr Coding & Reimbursement Analyst, Sue Rowinski Group LLC
March 19, 2014
Baltimore, MD
Bart Edward Muhs, MD, PhD
Assoc. Professor of Surgery (Vascular)
Co-Director, Endovascular Program
Yale School of Medicine, New Haven CT

## Slide 2: ICD10-PCS Coding Proposal: Aptus Heli-FX Procedure
Agenda
Heli-FX Clinical Benefit
Heli-FX Procedure Overview
Rationale for new ICD10-PCS Codes
ICD10-PCS Coding Request

## Slide 3: Aortic Aneurysms Have Two Treatment Options: Open Surgical and Endovascular Aneurysm Repair
Aortic Aneurysms:
Thoracic
Abdominal
Repair:
Open Surgical
Endovascular
CV
Endo Repair
Less morbidity
Durability?
Anatomical limitations
CV
Notes: Objective is to prevent rupture, open ‘definitive’ but highly invasive. EVAR has ‘endo minimally invasive’ benefits, but subject to more late aneurysm issues, requires life long f/u.
Open provides direct visualization, ability to see tissue and close leak, optimize anastomosis

## Slide 4: Endovascular Aneurysm Repair (EVAR): Now Most Common Procedure for Aortic Aneurysm Repair in US
By 2009, ≈45,000 elective aortic aneurysm repairs performed in US Medicare population.
Among > 30,000 infrarenal repairs ≈80% performed with EVAR.
Sachs T , et al. J Vasc Surg. 2011;54:881–888
1995 1997 1999 2001 2003 2005 2007 2009
Total
EVAR
Open
5,000
10,000
15,000
20,000
25,000
30,000
35,000
0
Notes: Patient and physician demand have made EVAR treatment of choice. Shorter hospital LOS, reduced procedural M&M, and faster recovery are offset by lifelong follow-up and frequent secondary interventions

## Slide 5: “Achilles Heel” of EVAR: Despite Advances in Endografts, Late Failure Remains, Life Long F/U Still Required
Loss of proximal neck seal and/or fixation = endoleaks, migration, aneurysm repressurization, enlargement, rupture
Most failure and 2nd interventions occur at proximal aortic neck
Presence of hostile prox neck increases risk of late complications, often contraindicates endo Tx option
Risk of complications continues through each year of follow-up.
Loss of fixation, seal
due to migration
Type 1 Endoleak

## Slide 6
R.M. Greenhalgh et al. N Engl J Med 2010, 10.1056/NEJM 0909305
Landmark EVAR-1 & DREAM Trials:
Higher Complications & 2nd Interven. in EVAR vs. Open Repair
De Bruin et al. N Engl J Med 2010;362:1881-9

## Slide 7: Proximal Neck Failure: The Most Frequent Cause for 2nd Interventions and Explantation
Wyss et al. Ann Surg 2010;252(5):805-12.
Turney et al. J Vasc Surg. (30 December 2013)
Proximal neck issues occur early and late and must be corrected when detected

## Slide 8: Hostile Prox Neck Compromises Acute, Early & Long Term Seal & Fixation: Commonly Seen in EVAR Patients
Large >28mm (Diameter)
Short <10-15mm (Length)
Conical Shape
Angulated
Excessive Thrombus & Calcium

## Slide 9: Heli-FX Endovascular Procedure Replicates the Gold Standard ‘Surgical’ Type Anastomosis

## Slide 10: Heli-FX System includes Anchors, Applier, and Guide Applier is Microprocessor Controlled, Guide is Steerable
Surgical-type anastomosis at proximal aortic neck (location of type Ia high-pressure endoleaks)
Physician determined location and number of fixation points/anchors
Similar versatility & limitations as open surgically sutured anastomosis (i.e. tissue strength, calcium, wall penetration)

## Slide 11: Aptus Heli-FX System 510(k) Cleared, CE Marked: Indicated for Leading Endografts
Intended to provide fixation and augment sealing between endovascular aortic grafts and aorta
Evaluated, determined compatible with Cook Zenith®, Gore Excluder®, Medtronic AneuRx®, Endurant® and Talent® (AAA), Cook Zenith TX2®, Gore TAG® and Medtronic Valiant® (TAA)
Cook Zenith®
Gore Excluder®
Medtronic AneuRx ®
Medtronic Endurant ®
Medtronic Talent ®
EndoAnchors shown here

## Slide 12: Heli-FX Procedure: Experience Demonstrates Growing Adoption
Clinical & Commercial Experience | 
Number of total Patients treated | > 2100
Number of EndoAnchors implanted | >10,000
Number of US Customers | >350 Hospitals
Specialties using Heli-FX | Vasc Surgeons, Int Radiologists & Cardiologists, CT Surgeons
AAA:TAA Case Ratio | Approx 10:1 to date
Primary EVAR* 77%
Revision EVAR*
23%
*US data only

## Slide 13: Heli-FX-Related Outcomes from STAPLE-2: EndoAnchors Result in More Sac Regression
EndoAnchors result in more sac regression (>80%) than standard EVAR despite shorter proximal necks
Sac stability is key determinant of success of EVAR

## Slide 14: ANCHOR Post-Market Registry
Principal Investigators | Dr William Jordan, University of Alabama, Birmingham (US) Dr Jean-Paul de Vries, St Antonius Hospital, Nieuwegein (NL) | 
Design | Prospective, observational, international, dual-arm registry Primary arm – EndoAnchors placed at time of endograft implant Revision arm – EndoAnchors placed as part of a later revision procedure | 
Protocol | EndoAnchor use per IFU, follow-up per standard of care | 
Duration | Five years follow-up | 
Primary Endpoints | Effectiveness | Successful implantation + freedom from migration / type Ia endoleak at one year
 | Safety | Freedom from device (Heli-FX) or procedure-related SAE at one year
Sites | 37 US / 18 EU | 
Patients Enrolled | 345 as of 1/31/14 (continuing up to 1,000 per study arm) | 

## Slide 15
ANCHOR Registry:
Case Mix Shows Widely Varied Usage & Endograft Types
Primary
N=260 (76%)
Revision
N=84 (24%)

## Slide 16: ANCHOR Registry – EndoAnchor Usage Add-on to EVAR and Stand-Alone
Procedure break-down:

## Slide 17
(1) At most distal renal artery
(2) >10% increase in diameter from most distal renal artery to 15mm below most distal renal
* Analysis based on available Core Laboratory data
 | All | Primary | Revision
Max Aneurysm Diameter [mm], mean (range) | 58.0 (24-98) | 55.9 (24-98) | 65.3 (34-93)
Neck Length [mm], mean (range) | 15.9 (0-57) | 16.3 (0-57) | 14.5 (2-44)
Necks ≤10mm Length, N (%) | 43% | 42% | 45%
Neck Diameter1 [mm], mean (range) | 27.0 (17-45) | 26.2 (17-45) | 29.5 (21-44)
Conical Necks2, N (%) | 60% | 59% | 61%
ANCHOR Registry - Anatomical Characteristics*
Indicates Some of Most ‘Challenging’ Anatomy Studied in EVAR

## Slide 18
Median # EndoAnchors Implanted* | 
Primary Arm: | 5
Revision Arm: | 6
Total Combined: | 6
Primary (n=260) | Concern for Late Failure | 147 (56.5%)
 | Treatment of Type 1a Endoleak | 59 (22.7%)
 | Prevention of Neck Dilation | 42 (16.2%)
Revision (n=84) | Type 1a Endoleak | 42 (50%)
 | Migration & Endoleak | 21 (25%)
 | Migration | 11 (13.1%)
ANCHOR Registry - Reason for EndoAnchoring
Prevention & Treatment of Late Failure Verifies Clinical Need
*EndoAnchors are permanently implanted; patients need to be followed long term

## Slide 19
Arm | N | Success | % Successful
Primary | 260 | 257 | 98.8%
Revision | 84 | 78 | 92.9%
Reasons for Unsuccessful Results:
Primary: 3 Unresolved type 1a endoleak at final angio, 2 resolved (1 @1-M & 1 @3-M F/Us respectively)
Revision (N=6): Persistent Type 1a endoleak at final angio, 2 Pts outside Aptus IFU
No EndoAnchor related SAEs or re-interventions
50% of type 1 endoleaks treated w/EndoAnchors also used Cuffs (53/106)
ANCHOR Registry – Acute Technical Success
Favorable Results Suggest Improvement Over ‘Standard of Care’
Notes: How were these outside IFU? Should they still be in Registry? I think yes

## Slide 20: ANCHOR Results Compare Favorably to Alternative Tx
Patients with Persistent Type 1a Endoleak at End of Primary EVAR procedure | 
Studies | Type 1a Endoleak
Byrne J et al.* (Patients treated with Palmaz Stent) | 8.6% (14/162)**
ANCHOR Registry | 1.6% (1/59)***
* Byrne J et al. Ann Vasc Surg 2013 May;27(4):401-11
** Rate includes both emergent and elective patients receiving Palmaz stents during primary EVAR procedure.
*** N = 59, 1 out of 59 Patients had an acute Type I endoleak unresolved at final angio
20
Meta-analysis of outcomes in AAA Endo Repair with hostile anatomy |  | Type 1 Endoleaks
Studies | Median Follow-Up | Hostile Necks
Meta-analysis, Antoniou et al* | 12-Months | 9.8% (20/205)**
ANCHOR Registry | 10.4-Months | 1.5% (3/189)***
* Antoniou GA et al. A meta-analysis of outcomes of endovascular abdominal aortic aneurysm repair in patients with hostile and friendly neck anatomy. J Vasc Surg 2012
** Hostile neck criteria: neck length <15 mm and neck angulation > 60 degrees
*** Hostile as determined by physician in Primary Arm

## Slide 21
EndoAnchors show favorable results as prophylaxis for late proximal seal complications
  99% technical success
  No Type 1a Endoleaks in 10-mo median F/U, despite high proportion of hostile necks
  Data consistent with STAPLE-2 IDE trial where all pts had EndoAnchors placed primarily
EndoAnchors show high effectiveness in treating acute and late Type 1a endoleaks (98% & 90% respectively)
Low re-intervention rates (0.4%) in the Primary Arm despite hostile anatomy
  Low Type 1a Endoleak rates (1.5%) in Primary compared to ~10% in hostile necks per meta analysis by Antoniou et al
ANCHOR Registry:
Favorable Conclusions from Early Results
Notes: I have a case of Type 1 EL at 1 month

## Slide 22: The EndoAnchoring Procedure

## Slide 23: Heli-FX Procedure Duration: Implant Time Varies with # of Anchors, Complexity of Anatomy, Familiarity of Physician
Recommended # EndoAnchors: | 4 EndoAnchors recommended for ≤29mm dia aortas 6+ EndoAnchors recommended for >29mm dia aortas EndoAnchor locations should avoid severe thrombus and calcium
Avg EndoAnchors Implanted: | During a Primary or Revision EVAR or TEVAR is 5 to 6
Add’l Operating Room Time: | 30-45 min (not including set up) required to implant EndoAnchors
Heli-FX Procedure: | EndoAnchor Procedure has its own distinct beginning, middle & end separate from the Endograft insertion & implantation May also be performed as a stand alone procedure (Repair without Endograft Extension Cuff)
Image Guided, Resource Intensive Procedure Completed in
OR, Cath Lab or Interventional Suite

## Slide 24: Anchoring Requires Advance Planning: Location(s) and C-Arm Angles for Fluoroscopy & Implant
Case Planning:
Case planning by physician includes CT scan review, measurements, review of 3D recon & planning for EndoAnchor implantation location(s) – iPad or hard copy
AAA Case – iPad used for Case Planning
TAA Case - Hard Copy Worksheet used for
Case Planning
C-Arm Used for EndoAnchoring
Positioning & Angulation

## Slide 25: Heli-FX Device Preparation (Pre-Insertion)
Device Packaging:
Product is unpacked &
Provided to sterile field
Device Preparation:
Saline flush all components
Turn Applier on
EndoAnchor Loading:
Load EndoAnchor
Verify loading

## Slide 26: Heli-FX Device Insertion: After Prep/Loading, Guide is Inserted
Insert Guide & Dilator into femoral artery
Advance & position
Into Guide at Proximal Neck of Aorta
Dilator & Guide entering Iliac
Dilator & Guide
At Proximal Neck
Heli-FX Guide

## Slide 27: Guide is Positioned, Applier is then Inserted and Advanced
Applier inserted
into Guide
Applier is advanced to proximal neck
Anchor Applier

## Slide 28: Heli-FX Implantation: Proper Positioning Highly Critical
90°
Stage 1
Press Applier Forward once to implant EndoAnchor halfway.
Confirm EndoAnchor tip penetrated thru endograft & Guide/Applier position remained stable
If acceptable, proceed to Stage 2. Otherwise, press Reverse button & attempt again. Re-position if necessary.
Stage 2
Maintain constant position & pressure throughout deployment sequence.
Press Applier Forward button again to fully implant EndoAnchor
Slowly retract Applier under fluoro to ensure EndoAnchor is fully released.
Repeat the above steps for each EndoAnchor (Avg. 5-6 per case)
Perpendicular Positioning
Rotate Guide to visualize “C” marker
Position Guide & Applier 90° relative to endograft
Apposition
Stabilize Guide. Advance Applier until resistance is felt against endograft & aortic wall.
Confirm perpendicular positioning & Guide recoiling against opposite wall under fluoro

## Slide 29: Heli-FX Device Insertion & Implantation of EndoAnchors
Guide is ‘deflected’ into position, Anchor
implanted

## Slide 30: Heli-FX Procedure as Add-On to EVAR (Parent Procedure)
Angiogram prior to EndoAnchoring Ensuring Proper Graft Location
Heli-FX Guide Advancement
1st Anchoring Location Selected w/ Guide
(C-Arm LAO 45°)
Heli-FX Applier Ready to Implant 1st EndoAnchor
4th EndoAnchor Implanted
Final Angiogram after EndoAnchoring
Applier Ready to Implant 4th EndoAnchor
(C-Arm RAO 45°)
Arrows Denote Implanted
3 EndoAnchors
Images courtesy of Dr. Burkhart Zipfel, Deutsches Herzzentrum Berlin

## Slide 31: FDA Classification

## Slide 32: Heli-FX Clinical Scenarios Vary According to Patient Need
Six (6) procedural use cases
 |  | EVAR (Body Section: Lower Artery) | TEVAR (Body Section: Heart & Great Vessel)
Heli-FX as Add-On | Primary | Control of acute Endoleak and/or Hostile anatomy | Control of acute Endoleak and/or Hostile anatomy
 | Revision | Control of Endoleak / repair of migration | Control of Endoleak / repair of migration
Heli-FX as Stand-Alone | Revision of previous aneurysm repair | Control of Endoleak | Control of Endoleak

## Slide 33: Heli-FX Procedure as Stand Alone (Parent Procedure)
EndoAnchoring Stand Alone Procedure
to Repair Endoleak
Endoleak
EndoAnchors

## Slide 34: Heli-FX as Add-On to EVAR (Parent Procedure)
Primary Challenging
Neck Anatomy
+ EndoAnchors
Primary or Revision
with Endoleak
+ EndoAnchors
Revision
with Cuff
+ EndoAnchors
Endoleak
Extension Cuff

## Slide 35: Revision Case w/a Type 1a Endoleak, Anchors
Type 1 Endoleak 1 week post implant
9 Heli-FX EndoAnchors implanted
Type 1 Endoleak
Resolved without cuff
Images courtesy of Bart Muhs, MD & Scott Aruny, MD
Yale New Haven Medical Center

## Slide 36
Pre-Op
9.5cm asymptomatic AAA, female
Reason for anchoring: highly angulated, short neck
Intra-Op
First completion with type Ia endoleak
Final Angio
Proximal cuff and 4 EndoAnchors
No endoleak at final angio or 30-day CTA
Final Angio
30-day CTA
Primary Endograft Case w/Acute Type 1a Endoleak
Case images courtesy of Will Jordan, MD, Univ. of Alabama

## Slide 37
Case images courtesy of Dr. Manish Mehta,
Albany Vascular
77 year old female
95mm saccular AAA
Short proximal aortic neck
Deployment of Medtronic Endurant
4 EndoAnchors
No endoleak at 30-day CT
Primary Endograft Case with Challenging Anatomy

## Slide 38: Heli-FX TAA Procedures
Primary Prophylactic Proximal &
Distal shown
Primary or Revision
with Endoleak
Primary or Revision
with Cuff
Extension Cuff
Endoleak (s)

## Slide 39
Case images courtesy of P Kasprzak MD, Regensburg
Final Angio, leak resolved
Type 1a Endoleak after Endograft implantation
4 EndoAnchors implanted
Primary TEVAR – Short Proximal / Distal Necks
Mal-apposition

## Slide 40: Rationale for New ICD10-PCS Qualifier & Codes
NTAP Application is under consideration for FY2015
Cleared by the FDA not as a suture but as a Medical Device to:
  Repair failed endografts
  Improve an endograft’s inherent fixation and sealing mechanisms, especially in patients with challenging neck anatomy
Distinct procedure with its own beginning, middle & end from that of the endovascular graft procedure
Requires unique & patented instruments for EndoAnchor deployment
  EndoAnchor
  Heli-FX Guide
  Heli-FX Applier
Requires additional operating room time of 30-45 minutes (not including set up time) to implant 5-6 EndoAnchors into the wall of the abdominal or thoracic Aorta

## Slide 41
Used with most commercially available endografts as a Supplement or in a Repair
Need to address the multiple root operations occur during Primary & Revision EVAR and TEVAR
  Implantation of multiple intraluminal devices (graft, cuff, Heli-FX),
  Each serving different purposes during the same surgical session
No distinct ICD9 -CM codes, therefore it is not possible to convert to ICD10 -PCS using GEM mapping
Heli-FX is a new technology:
  No comparable ICD9-CM, ICD10-PCS codes exist because there is no other FDA approved implantable device which serve the same function
Rationale for New ICD10-PCS Qualifier & Codes

## Slide 42: ICD10-PCS Coding Proposal Summary
Proposing the creation of (1) qualifier and new and separate codes for the Heli-FX when performed in the abdominal and thoracic regions. Root Operations for these regions could be:
  Lower Artery body section
    Supplement - Heli-FX is an add-on procedure during primary/revision EVAR
    Repair - Heli-FX is the parent procedure during revision EVAR
  Heart and Great Vessel body section
    Supplement - Heli-FX is an add-on procedure during primary/revision TEVAR
    Repair - Heli-FX is the parent procedure during revision TEVAR (emerging procedure)
Establish the Qualifier T, EndoVascular Graft Fastener
To help coders quickly locate the new ICD10-PCS qualifier and codes
  Place in the Medical/Surgical Section
  Add the Heli-FX EndoAnchor System to the Device Key because it is a new technology

## Slide 43: Coding Issue
Currently there no ICD9-CM and ICD10-PCS codes to capture the
Heli-FX Stand-alone and Add-on procedures during EVAR and TEVAR
 |  | EVAR | TEVAR
Heli-FX Add-On Procedure | Primary | Control of acute Endoleak and/or Hostile anatomy | Control of acute Endoleak and/or Hostile anatomy
 | Revision | Control of Endoleak / repair of migration | Control of Endoleak / repair of migration
Heli-FX Stand-Alone Procedure | Revision of previous aneurysm repair | Control of Endoleak | Control of Endoleak

## Slide 44
Heli-FX is used with most commercially available endografts in multiple operations as outlined in Options 2-4 and initial ICD10 Application.
  Operations are Introduction, Supplement, in a Revision or in a Repair
Distinguish and capture the Heli-FX Stand-alone and Add-on procedures.
There are no distinct ICD9-CM codes for Heli-FX Stand-alone and Add-on procedures, therefore conversion into ICD10-PCS using GEM mapping is not possible
Heli-FX is a new technology:
  No comparable ICD9-CM, ICD10-PCS codes which exist because there is no other FDA approved implantable device which serves the same function as the Heli-FX system.
Rationale for new ICD10-PCS Codes

## Slide 45: ICD10-PCS Coding Request Summary
Option 4
  Create a new device character
  Because Heli-FX is a new technology add the Heli-FX System to the Device Key
Heli-FX Procedure | Lower Artery, Abdominal | Heart and Great Vessels, Thoracic | Section
Stand-alone during Revision EVAR or TEVAR | Operation: Revision | Operation: Revision | Medical- Surgical
Add-on during Primary EVAR and EVAR | Operation: Supplement, | Operation: Supplement | Medical -Surgical
Add-on during Revision EVAR and TEVAR | Operation: Revision | Operation: Revision | Medical-Surgical

## Slide 46
Conclusion
Heli-FX is a new & unique technology with significant clinical benefit as a stand alone and as an add-on in EVAR & TEVAR
There are no other existing codes which are applicable to Heli-FX
Heli-FX requires additional planning, operative steps, additional time, resources, and associated risks & therefore warrants its own specific coding

## Slide 47: Thank you